## Slide 1: Silicone Molding and Resin Casting Small Parts
Kate Szkotnicki
Kansasfest 2016

## Slide 2: Agenda
Silicone Mold Making Materials
Silicone Mold Making Demo
Resin Casting Materials Needed
“Casting” Demo
Q/A

## Slide 3: Mold Making: Materials

## Slide 4: A/B Silicone
Different makes
Some are food-safe
Some are 1:1, some are other ratios
All require CAREFUL MEASURING AND MIXING
“Pot Time” – how long you have to work

## Slide 5: Mold Box
Should be ½” around all sides of your part/parts
Needs to contain a liquid
Several options
  Legos/Clay
  Plexiglass and Hot Glue
  Styrofoam

## Slide 6: Clay
Optional for 1-part molds
  Sealer
Required for 2-part molds
  Make half a mold at a time
Needs to be inert
  Sulfur Free

## Slide 7: Other Supplies
Disposable Supplies
  Mixing container(s)
  Paint stir sticks
Reusable Supplies
  Mold Key Makers (acorn nuts, marbles)
  Release Agent
  Digital Scale

## Slide 8: Mold Making Demo (1-piece)
Build Box
Attach part to box securely
Seal box if needed
Measure A and B (equal amounts in this case)
Mix once
Pour into second container, mix again
Slowly and carefully pour mold
Let cure

## Slide 9: Resin Casting: Material

## Slide 10: Resin
Comes in 2 parts
  Resin
  Catalyst
  Some are 1:1, others use higher ratios
Different Chemical Formulae
  Polyester
  Polyurethane
  Epoxy

## Slide 11: Resin Continued
Many different brands
  Craft Grade (Castn’Craft)
  Model Making
  Prototyping
  Fiberglassing
Read Information
Try it first!

## Slide 12: Other Materials
Heat-Safe Disposable Container
  Aluminum Cans
  NO WAX
Disposable mixing sticks
Mold Release
Rubber Bands

## Slide 13: Safe Casting
Safety Gear
  Eye Protection
  Respirator/mask
  Disposable gloves
Work outside or in a well-ventilated area
Some are more dangerous than others

## Slide 14: Resin Casting Steps
Work in a well-ventilated area with safety gear
Clean and dress molds (mold release)
  Put 2-part molds together with bands/tape
Mix resin according to directions
  Sometimes you need more catalyst
  May not get it on the first try!
Pour slowly
Allow to cure

## Slide 15: Special Resin Considerations
Pressure Casting
  Allowing the piece to cure in a pressure vessel
  Avoids surface air bubbles
  Needs special equipment (pressure pot, compressor)
Parts don’t come out ready
  May probably need sanding/polishing
  Wet or dry sand
  Polyester will be tacky on the exposed parts

## Slide 16: “Resin” Casting Demo
Not really
Jello Gummy Candy 
Same technique, safer material for demo

## Slide 17: Questions/Answers?