## Slide 1: NadaNet Networking for Apple II Programmers
Michael Mahon

## Slide 2: Why NadaNet?
In the early 1990s, I became interested in “clustered” machines: parallel computers connected by a LAN.
This interest naturally turned to Apple II computers, and the possibility of an all-software Apple II network.
Preliminary work indicated that data rates of several kilobytes/second were possible using a digital phase-locked loop, adequate for an Apple II cluster.
It seemed like a great opportunity to “reinvent” Ethernet and learn from the bottom up!

## Slide 3: What is NadaNet?
A peer-to-peer baseband serial bus network
Implemented entirely in Apple II software
Both Applesoft and M/L APIs
Contention-based, with collision avoidance (CSMA/CA)
Connecting dozens of Apple II’s
>10K bytes/second bandwidth
1 to 256-byte packets
1 to 64K-byte atomic data transactions
A network to support
parallel programming on Apple II’s.

## Slide 4: What NadaNet is Not
A way of connecting to the Internet
A way of connecting to non-Apple II’s
Compatible with TCP/IP networks

## Slide 5: NadaNet Requirements
Two or more Apple II’s
Each machine requires a game port adapter
  16-pin internal port (not 9-pin joystick port)
  The Apple II and II+ allowed a short network without an adapter, but later machines present heavier loads.
Adapters are simple and can be built easily
Adapters extend the physical length of the network
  250 feet if shielded cable used
  500 plus feet if Cat 5 UTP used

## Slide 6: NadaNet Adapter

## Slide 7: Fixing late-model //e’s
Just snip one (or both) leads on each capacitor to restore full bandwidth capability to pushbutton inputs.
Can snip one lead and lift cap slightly for minimal mod.
  Can always be re-soldered to handicap your Apple!
0.1 uF capacitors to ground were added in “Platinum” board revision as a brute-force EMI fix.

## Slide 8: How is it used?
NadaNet is loaded and initialized
  BLOAD from disk and initialize, usually by HELLO or STARTUP
  (or boot from network)
Machines are only “on” the net when they are “serving”--listening for packets and acting on them.
Any machine can process requests while it is serving.
Any machine can make requests at any time, but they will only be acted upon if the target machine is serving.
  Default request timeout is ~3 seconds.
If a Message Server is serving, messages can be sent and received at any time.

## Slide 9: NadaNet Request APIs
&PEEK (dest,addr,len16,locaddr)
&POKE (dest,addr,len16,locaddr)
&CALL (dest,addr [,ax])
&PUTMSG (msid,mclass,mlen8,maddr)
&GETMSG# (msid,mclass,mlen8,maddr)
&PEEKINC (dest,addr,incval16,oldval16)
&BPOKE (addr,val16)
&SERVE# (iter)
  Until 1 request, iter*20ms timeout, or key is pressed
CALL 973
  Serves indefinitely

## Slide 10: Machine 10 Demo Program
100 REM NadaNet Hi-res Demo
110 REM MJM - June 23, 2007
120 :
130 D$ = CHR$(4)
140 PRINT CHR$(21) : REM 40-Col mode
150 HGR2
160 PRINT D$”BLOAD NADAHGR”
170 CALL 973 : REM Serve “forever”

## Slide 11: Examples
&PEEK (10,2*4096,2*4096,2*4096)
  Moves $2000 bytes from machine 10’s HGR1 buffer to our HGR1 buffer, where we can see it.
&POKE (10,4*4096,2*4096,2*4096)
  Moves $2000 bytes from our HGR1 buffer to machine 10’s HGR2 buffer, replacing its contents.

## Slide 12: POKE: A Typical Protocol
POKE Request
POKE Ack
Data packets
Data Ack/Nak
...
8
8
256
256
?
8
Optimization:
Data packets and Data Ack are omitted if length is 1 or 2 bytes.

## Slide 13: Control Packet Format
Request
Request
Modifier
Dest
From
Address
Length
Cksum
Request identifies all control packets of a given request type
  PEEK, POKE, CALL, etc.
Modifier specifies the role of the packet in the protocol
  Request, Request Ack, Data Ack, Nak
Dest identifies the target machine
From identifies the sending machine
Address (generally) specifies a target machine address
Length (generally) specifies a data length
Cksum is an EOR checksum applied to all packets
Control packets are ~1ms long.

## Slide 14: Nadanet Data Format
Locked
or Idle
ONE
8 cy
ZERO
16 cy
ONE
31 cy
ZERO
8 cy
ONE
8 cy
Bit 7
8 cy
Bit 6
8 cy
...
Bit 1
8 cy
Bit 0
8 cy
ZERO
22-23 cy
ONE
8 cy
Bit 7
8 cy
Bit 6
8 cy
...
...
Bit 1
8 cy
Bit 0
8 cy
ZERO
(Idle)
...
End of
checkbyte
Packet end:
Interbyte separator:
Start of packet:
Servo edge
Servo edge
Coarse sync
Start sync
30-31 cy
71 cy

## Slide 15: NadaNet Arbitration
Always listen before sending
Wait for net to be idle for 1 millisecond + id * 22cy
  Lower id machines have higher arbitration priority
Seize net by forcing ONE state
Consequences:
  Network is “locked” until it is idle for longer than 1ms.
  All requests meet this requirement and so are atomic.

## Slide 16: AppleCrate
An 8-machine Apple //e cluster
ROMs modified for NadaNet boot (from server)
Powered by PC power supply

## Slide 17: Questions and discussion...