## Slide 1: Real Sound for 8-bit Apple II’s
Michael Mahon

## Slide 2: The Apple II speaker (and cassette output)
Can only toggle “1-bit output”
Can’t choose “polarity”
Doesn’t respond to alternate low-frequency toggles

## Slide 3: Simple Sound
Double-frequency timing loop
  Squarewaves (beep, etc.)
Actual frequency timing loop
  Non-50% duty cycle, timbre (Red Book)
Infinitely-clipped 1-bit sound
  Distorted speech and music (Hex Dump Reader, Audex, etc.)

## Slide 4: Complex Sound
Ultrasonic timing loop with variable duty cycle pulses
  Electric Duet (4 duty cycles = 2-bit precision)
  Software Automatic Mouth (?)
  Sampled sound (many duty cycles)

## Slide 5: Variable Duty Cycle

93 cycles
63
03
02
01
00
Sample value
70
23
83
10
84
9
85
8
86
7


## Slide 6: Software DACs
Sample rate (11.025kHz)
Pulse rate (11.025kHz / 22.05kHz)
Bits of precision (3, 4, 5, 6)

## Slide 7: Timing Constraints
11kHz = 93 Apple II cycles/sample
  1/93cy = 10.973kHz, -52Hz, -0.005%
  1/92cy = 11.092kHz, +67Hz, +0.006%
Apple II timing resolution = 1 cycle
4 cycles required to flip speaker
  8 cycles per pulse, 4-cycle minimum width
Sound amplitude = width / period

## Slide 8: Software DAC loop example first try: constant 93 cycles, 6-bit precision
loop: 4 [Start pulse] 3 JMP vector1 <0-63 Variable delay> 4 [End 7-70 cycle pulse] 3 JMP vector2 <63-0 Complementary variable delay> 5 Fetch next sample 2 Check for end (if =0) 10 Increment ptr,Y 6 Shift sample 4 Get vector1 4 Set vector1 2 Transform vector1--> vector2 4 Set vector2 3 JMP loop
117 cycles ** 24 cycles too long! **

## Slide 9: DAC611 Constant 93 cycles, 93-cycle pulse period, 6-bit precision
loop: 4 [Start pulse] 6 Get vector1 4 Set vector1 3 JMP vector1 (-->long: if >$7F) <2-33 delay> 4 [End 19-50 cycle pulse] 4 Transform vector1-->vector2 4 Set vector2 3 JMP vector2 <33-2 complementary delay> 10 Increment ptr,y 5 Fetch next sample 2 Test for end if =0 6 Shift 3 3 JMP loop 93 cycles
long: 17 (entered at +17 cycles) <2-33 delay> 11 Increment ptr,y 4 Transform vector1-->vector2 4 Set vector2 5 Fetch next sample 2 Test for end if =0 6 Shift 3 4 [End 51-82 cycle pulse] 3 JMP vector2 <33-2 complementary delay> 2 NOP 0 [falls into loop] 93 cycles
Pulse frequency of 11kHz is intolerable to many listeners.
[Greg Templeman, 1993]

## Slide 10: DAC522 Constant 92 cycles, 46-cycle pulse period, 5-bit precision
Logically 32 separate pulse generators
  Each generates two pulses in 92 cycles
  Each fetches next sample and sets vector
  Then it vectors to next generator
  Computation is distributed between pulse edges
Pulse frequency of 22kHz is inaudible!

## Slide 11: DAC522 Pulse Generators

46 cycles

46 cycles
9
37
37
9
37
9
9
37
38
8
8
38
39
7
7
39
40
6
6
40
31
03
02
01
00
Sample value


## Slide 12: Other Problems
Starting and stopping without “pops”
  Solution: Don’t stop!
    “Ramp” waves to start and stop at 0 level
    generate continuous 0-level pulses (except for key clicks)
Generating long sounds at 11kB/second
  Solution: Direct Digital Synthesis
    Resample wavetables on-the-fly
    Use envelope table for dynamics

## Slide 13: RT.SYNTH Single-voice multi-timbral real-time wavetable synthesizer
Voice waves are resampled on-the-fly to note frequencies
  Frequency = Integer.fraction sample index increment
Can support as many different voices as fit in memory
  A voice is represented as a set of single-cycle waveshapes selected by a table representing the envelope of the voice.
  This supports
    Tonal voices with complex attacks that are resampled
    Atonal sounds that are played as “waves”
Wavetable waveforms are stored starting and ending at zero amplitude to minimize pops
“Resting” or idling sound is the zero-level pulse train

## Slide 14: DAC522 Generator Code
0800: 8D 30 C0 >6 gen0 sta spkr ; <==== start time: 0
0803: EA >7 nop ; Kill 2 cycles
0804: 8D 30 C0 >8 sta spkr ; <===== stop time: 6
0807: 85 EB >9 sta ztrash ; Kill 3 cycles
0809: E6 ED >10 inc scount ; Compute envelope
>11 ciny
080B: F0 01 >11 beq *+3 ; If =, branch to iny
080D: A5 >11 dfb $A5 ; "lda $C8" to skip iny
080E: C8 >11 iny
>11 eom
080F: 18 >12 clc
0810: A5 EC >13 lda frac ; Compute next sample
0812: 65 FE >14 adc freq
0814: 85 EC >15 sta frac
0816: 8A >16 txa
0817: 65 FF >17 adc freq+1
0819: AA >18 tax
081A: B1 06 >19 lda (env),y ; Next sample page
081C: 8D 30 C0 >20 sta spkr ; <==== start time: 46
081F: EA >21 nop ; Kill 2 cycles
0820: 8D 30 C0 >22 sta spkr ; <===== stop time: 52
0823: 85 EB >23 sta ztrash ; Kill 3 cycles
0825: 8D 2A 08 >24 sta :ptr+2
0828: BD 00 00 >25 :ptr ldaa 0*0,x ; Fetch sample.
082B: 8D 3C 08 >26 sta :sw0+2
082E: C6 FC >27 dec dur ; Decrement duration
>28 cdec dur+1
0830: F0 02 >28 beq *+4 ; If eq, branch to dec
0832: EA >28 nop ; Else kill 2 cycles and
0833: AD >28 dfb $AD ; "lda xxxx" to skip dec
0834: C6 FD >28 dec dur+1 ; of zero-page param.
>28 eom
0836: A5 FD >29 lda dur+1
0838: F0 03 >30 beq :quit ; Finished.
083A: 4C 00 00 >31 :sw0 jmp 0*0 ; Switch to gen, T = 89
>32
083D: 4C 40 09 >33 :quit jmp quit

## Slide 15: CRATE.SYNTH 8-voice multi-timbral MIDI playback wavetable synthesizer
Uses AppleCrate machines as eight digital oscillators
MIDI.COMPILER
  Merges multi-stream MIDI events
  Tempo changes complicate timekeeping
  Schedules 8 digital oscillators in one pass
  Tries to re-use oscillators with a voice history
  When >8 oscillators needed, “steals” from oldest note
CRATE.SYNTH
  Uses NadaNet to load the 8 oscillator machines
  Starts them all in sync (AppleCrate drift is ~1 ms. in 40 sec.)

## Slide 16: Questions and discussion...