## Slide 1: AppleCrate II
Michael Mahon
Notes: <number>

## Slide 2: Why AppleCrate?
In the early 1990s, I became interested in “clustered” machines: parallel computers connected by a LAN.
This interest naturally turned to Apple II computers, and the possibility of creating an Apple II “blade server”.
A lucky eBay bid in 2003 netted me 25 Apple //e main boards (14 enhanced) for $39, including shipping!
“Because it can be done!”
Notes: <number>

## Slide 3: AppleCrate I
An 8-machine Apple //e cluster, all unenhanced machines.
ROMs modified for NadaNet boot (from server)
Powered by PC power supply
Fine for a desktop, but quite fragile for travel!
Notes: <number>

## Slide 4: Why AppleCrate II?
Out of the 25 main boards, 14 were Enhanced //e’s.
  Only 512 bytes of self-test space in ROM required a new “passive” network boot protocol.
I wanted a ‘Crate that was mechanically robust and compact enough to travel.
I wanted to scale it up to 16 machines, and incorporate a “master” for convenience.
I wanted better quality sound output.
A machine to support
parallel programming on Apple II’s.
Notes: <number>

## Slide 5: AppleCrate II
17 Enhanced //e boards
  1 “master” and 16 “slaves”
  Self-contained system
I/O can be attached to the top board, so it is the “master”
All boards stacked horizontally using standoffs for rigidity
Total power ~70 Watts
  ~4.2 Watts per board!
17-channel sound
  External mixer / filter / amplifier
GETID daisy chain causes IDs to be assigned top-to-bottom
Notes: <number>

## Slide 6: Parallel Programming
The fundamental problem is maximizing the degree of concurrent computation to minimize time to completion.
To achieve that it is necessary to decompose a program into parts that:
  Require sufficient computation so that communication cost does not dominate TTC
  Are sufficiently independent so that communication does not dominate TTC
  Do not leave a few large/long sequential tasks whose computation will dominate TTC
Notes: <number>

## Slide 7: Pipeline Parallelism
Processing is divided into “phases” or “stages” that:
  Require approximately the same time to completion
  Can be performed essentially independently on many different data sets
Balancing the times required by each stage independent of the data can be difficult.
  The pipeline runs at the speed of the slowest stage.
  A problem in any stage is a problem for the whole pipeline.
This approach can be compared to an assembly line.
Notes: <number>

## Slide 8: Process Parallelism
Processing is divided into separate processes that:
  Can take any amount of time or resource
  Can be performed independently on different data sets
  Any particular data set may have a unique path through the network of processes.
  Data sets (“jobs”) queue for each process
Balancing processing resources to minimize queueing can be very difficult.
This approach can be compared to scheduling a machine shop floor.
Notes: <number>

## Slide 9: Data Parallelism
Some problems naturally “fall apart” into many nearly identical independent pieces that:
  Are sufficiently fine-grained that none dominates TTC
  Can be easily aggregated to balance computation with communication
These problems are “made to order” for parallel computation, since decomposition is trivial.
Often so easy it’s known as “embarrassing parallelism”
Notes: <number>

## Slide 10: Examples of Data Parallelism
Monte Carlo simulations
Database querys
Most transaction processing
  But must still check for independence
Mandelbrot fractals
Notes: <number>

## Slide 11: BPRUN (Broadcast Parallel Run)
RUNs an Applesoft program on all serving machines
Performs standard AppleCrate initialization
  Takes census of serving machines
  Boots any machines awaiting boot
  Re-takes census
Starts Message Server if needed
For each serving ‘Crate machine, &POKEs amd &CALLs the BPRUNNER program at $200
Broadcasts the BASIC program using “boot hack”
Registers “check-in” of machines running program
Loads and starts all slave machines in parallel.
Notes: <number>

## Slide 12: Parallel Mandelbrot
Each point is completely independent!
A “job” could be anything from a single point to all 53,760 points!
  I chose 280 points, or a line, for each “job”
The master machine queues jobs (in random order)
Each idle slave machine:
  Takes the first job in the job queue,
  Executes the computation, and
  Enqueues the result for the master to display
The result is an almost linear increase in the speed of execution.
Notes: <number>

## Slide 13: Mandelbrot Master
2180 REM Job parameters
2190 N = 192 : P = 20 : REM 192 jobs, max of 20 at a time
2200 JN = 0:RN = 0:SCH = 0 : REM Start empty
2210 :
2220 REM Build and maintain job queue
2230 IF JN < N AND SCH < P THEN GOSUB 2400: REM Sched another job
2240 IF RN < N THEN GOSUB 2500: REM Get result of job
2250 IF RN < N GOTO 2230
2260 :
2270 PRINT CHR$ (7)"All jobs completed."
2320 END
2330 :
2400 REM Schedule new job
2410 JN = JN + 1
2430 POKE BUF,LM%(JN - 1): REM Line number
2440 & PUTMSG (2, JQ, 8, BUF) : REM Enqueue job in JQ
2460 SCH = SCH + 1
2470 RETURN
2480 :
2500 REM Receive and display job result
2560 & GET MSG# (2, RQ, LL, BUF) : REM Get result from RQ
2570 IF PEEK(1) THEN FOR I = 1 TO 100: NEXT I: RETURN : REM Delay if no result
2580 SCH = SCH - 1:RN = RN + 1 : REM One less thing to do, one more thing done.
2590 PY = PEEK (BUF)
2600 H = INT (PY / 8):L1 = PY - H * 8 : REM Compute start of HGR2 line PY
2604 L3 = INT (H / 8):L2 = H - L3 * 8
2606 LINE = 4 * 4096 + L1 * 1024 + L2 * 128 + L3 * 40
2607 FOR I = 0 TO 39: POKE LINE + I, PEEK (BUF + 2 + I): NEXT I : REM Display line
2610 RETURN
You can see why it’s called embarrassing parallelism!
Notes: <number>

## Slide 14: RatRace
A “pure communication” program
Each slave is associated with a Message Server input queue
The queues are “primed” with three messages each
Each slave machine:
  Gets the first message from the queue,
  “Ages” the message by 1, and
  Puts the message on a random recipient’s queue
    Until each message has been passed 50 times
2850 messages are sent and received!
Notes: <number>

## Slide 15: RatRace Program
600 REM Message passing loop
610 & GET MSG#(2,IQ,L,BUF): REM Receive a message
630 IF NOT PEEK (1) GOTO 700
640 PRINT CHR$ (7);: REM Delay 100 ms. & flash LED
650 K = K + 1: REM Timeout counter
660 IF K < 50 GOTO 600
680 END : REM If 15 seconds w/o message.
690 :
700 REM Increment message age and pass it on...
710 K = 0: REM Reset timeout counter
740 S = PEEK (BUF + 1): REM Message "age"
750 IF S = 50 GOTO 600: REM Max trips--it stops here.
760 POKE BUF + 1,S + 1: REM Inc age by 1 and send it on.
770 D = INT ( RND (1) * NC) + 3: REM Random destination, 3..NC+2
800 & PUTMSG#(2,Q + D,20,BUF)
820 IF NOT PEEK (1) GOTO 600
830 PRINT "PUTMSG err."
840 END
All communication, no computation.
Notes: <number>

## Slide 16: Crate.Synth: Master
Performs standard AppleCrate initialization
Reads music file containing voice tables and music streams for each “oscillator” machine
Loads needed voices and music into each slave
Loads synthesizer into each slave and starts it (waiting for &BPOKE)
Starts all slaves in sync when requested
This process could benefit substantially from parallel loading.
Notes: <number>

## Slide 17: Crate.Synth: Slaves
Waits for master’s &BPOKE to start
Fetches commands from music stream that:
  “Rest” for T samples (11,025 samples/second), or
  “Play note N for T samples in current voice, or
  Change to voice V, or
  Stop and return to SERVE loop.
Any oscillator can play any voice at any time.
Notes: <number>

## Slide 18: Questions and discussion...
Notes: <number>

## Slide 19: POKE (A Typical Protocol)
POKE Request
POKE Ack
Data packets
Data Ack/Nak
...
8
8
256
256
?
8
Notes: <number>

## Slide 20: Control Packet Format
Request
Request
Modifier
Dest
From
Address
Length
Cksum
Request identifies all control packets of a given request type
  PEEK, POKE, CALL, etc.
Modifier specifies the role of the packet within the protocol
  Request, Request Ack, Data Ack, Nak
Dest is the target machine ID
From is the sending machine ID
Address (generally) specifies an address in the target machine
Length (generally) specifies a data length
Cksum is an EOR checksum of all bytes in the packet
Control packets are ~1ms long.

## Slide 21: Nadanet Data Format
Locked
or Idle
ONE
8 cy
ZERO
16 cy
ONE
31 cy
ZERO
8 cy
ONE
8 cy
Bit 7
8 cy
Bit 6
8 cy
...
Bit 1
8 cy
Bit 0
8 cy
ZERO
22-23 cy
ONE
8 cy
Bit 7
8 cy
Bit 6
8 cy
...
...
Bit 1
8 cy
Bit 0
8 cy
ZERO
(Idle)
...
End of
checkbyte
Packet end:
Interbyte separator:
Start of packet:
Servo edge
Servo edge
Coarse sync
Start sync
30-31 cy
71 cy
Notes: <number>

## Slide 22: NadaNet Arbitration
Always listen before sending
Wait for net to be idle for 1 millisecond + ID * 22cy
  Lower ID machines have higher arbitration priority
Seize net by forcing HIGH state
  Only 11-cycle sample-to-seize window for idle net collisions
Consequences:
  Network is “locked” until it is idle for longer than 1ms.
  All requests satisfy this requirement and so are atomic.
Notes: <number>