## Slide 1: APPLE ///
A Closer Look
Notes: <number>

## Slide 2: Introduction
Announced on May 19, 1980 at the National Computer Conference in Anaheim, California and shipped to dealers in June
Became available in limited quantities at retail in the fall of 1980, but it wasn't until spring 1981 that volume shipments began
A revised 5-volt edition was introduced in the fall of 1981, intended to address numerous problems
A redesigned and greatly improved model, the Apple III+ was introduced in December 1983

## Slide 3: Specs
SynerTek 6502A processor at 2 MHz
128K RAM (later 256K), supporting up to 512K
Display: Color Composite, Digital XRGB
16 Colors at 280 x 192, 16 Shades at 560 x 192 (same in B/W)
3 text modes: 40 column, 80 column, 40 column colored text (each letter, and each background could be any of 16 colors)
1 Internal 140K 5.25” floppy drive
Minimal ROM code
User-definable character sets

## Slide 4
Ports: 2 Serial, 1 external floppy supporting up to 3 external Disk /// floppy drives
Sound: 6-bit audio out
Internal Expansion: 4 slots, electrically compatible with Apple II slots
Apple II mode: emulates a 48K Apple II
$7800 (initial price), revised III: $3495, III+: $2995

## Slide 5: Worst. Apple. Ever. (AppleMatters.com This Week in Apple History Podcast: Worst. Apple. Ever.)

## Slide 6: What did Apple think?
”It just wasn’t a good enough machine and it had so many flaws from the start that when we reintroduced it we should have called it the Apple IV.”
- Woz
“[We lost] infinite, incalculable amounts.”
- Steve Jobs

## Slide 7: “"The Apple III was kind of like a baby conceived during a group orgy, and [later] everybody had this bad headache and there's this bastard child, and everyone says, 'It's not mine.'“ - Randy Wigginton “It would be dishonest for me to sit here and say it’s perfect.” - Mike Markkula

## Slide 8: Case Design
Heavy cast aluminum case intended to act as a heat sink
Designed by Steve Jobs without consulting the engineering team
Fan-free design because Jobs felt fans were “noisy and inelegant”
  Led to board failure brought on by overheating.
Forced the engineers to redesign the board layout to fit the case
Manufactured by a company that normally made engine blocks for automobiles

## Slide 9: Board Design
Due to the redesign forced by Jobs, board traces were too close together, leading to shorting
Non-gold connectors
Flaw in manufacturer’s flux washing process led to corrosion
Problems with sockets led to chips loosening during transport
  20% of all Apple ///’s shipped in 1980 arrived DOA

## Slide 10: Clock Chip (AppleMatters.com This Week in Apple History Podcast: “What Time Is It? I Have No Idea – I Use An Apple III”)

## Slide 11
National Semiconductor clock/calendar chip began failing
Month would show as “???”, hour would often go to “30” or “40” before rolling over
Apple removed the chip on all ///’s after February 1981, offered rebates
Later started selling a separate “upgrade kit” for $50
No explanation was ever given

## Slide 12: Software
Very little software was ready when the /// shipped
  VisiCalc /// was the only third-party application available for several months.
  Apple’s own word processor, Apple Writer /// didn’t ship until Fall 1981
Early versions of SOS and Business BASIC were buggy. SOS was a memory hog

## Slide 13
Pascal wasn’t released until late 1981. COBOL and Fortran repeatedly missed ship dates
The “Developer Problem” – who wants to
develop for a buggy machine?
SOS was considered complicated and hard to use
  Users took to pronouncing it “S-O-S” rather than “sauce” as Apple had hoped

## Slide 14
Underpowered?
Missing features users felt should come in a business-class personal computer
No internal hard drive
No Pascal or other high-level language in ROM
No high-resolution color monitor to take advantage of improved graphical specs and in-built RGB
No 68000 chip

## Slide 15
When is emulation not emulation?
An emulation mode was included to allow users access to the Apple II’s software library
Emulation requirement seriously limited Sander’s options for development (6502 vs 68000, etc)
Additional circuitry was added to limit emulation capability
  No access to extended memory, improved graphics or 80-column modes
Apple wanted users to think of the /// as a “serious” computer
Didn’t want to cut into Apple II sales
Want to play games? Get an Apple II

## Slide 16
SOS and ProDOS
Many concepts and techniques introduced in SOS live on in ProDOS
  Prefixes and Pathnames
Second block of a ProDOS boot disk contains Apple /// SOS boot loader
Everything is viewed as a device
  Most expansion cards made for the II can be made to work with the ///
  Device driver and fit

## Slide 17
Discontinuation
Apple tried to revive the /// with the ///+ but sales remained flat
Steve Jobs had already decided that Macintosh represented the future of Apple
Apple /// line quietly discontinued on April 24, 1984
Final estimated installed base was 75,000 (65,000 Apple ///’s plus 10,000 ///+ machines)

## Slide 18
Life After Death
User groups and magazines
  Washington Apple Pi, Call-A.P.P.L.E., On Three continued to provide support long after Apple killed the ///
  On Three was the only source for the 512K memory boards and other /// add-ons and hardware post-Apple
Sun Remarketing
  Did the same thing they would do later with Lisa hardware
  As late as 1995, you could get a nicely outfitted /// for less than $500

## Slide 19
Today’s Apple ///
Emulation
  MESS and SARA
Hardware Projects
  Apple3 List
  CFFA
  Disk II on a ///

## Slide 20
Recommended Reading
And Online Resources
Washington Apple Pi
  http://www.wap.org/a3
  Apple /// Archive DVD and Apple /// in 10 EZ Lessons DVD
Apple3.org
Apple3-L mailing list
  http://news.altair.com/mailman/listinfo/apple3-l
Call-A.P.P.L.E.
    http://applearchives.org/apple/